Recommended NDACC NASA Ames Format 2160 for ozonesonde data:

The working group recommends that you include as many of the “nice” variables as possible.

We make no recommendation concerning the “optional” variables.

Independent variables:

1st unbounded variable:   Station name

2nd bounded variable:     Time after launch [s]

Dependent variables (in black: essential, in blue: nice, in red: optional):

- Pressure [hPa]

- Geopotential height [gpm]

- Temperature [K]

- Relative humidity [%]

- Ozone partial pressure [mPa]

- Horizontal wind direction [decimal degrees] (range: 0– 360)

- Horizontal wind speed [m/s]

- GPS geometric height [m]

- GPS longitude [decimal degrees E] (range: 0.00 – 359.99)

- GPS latitude [decimal degrees N]

- Internal temperature [K] (box or pump)

- Ozone raw current [microA]

- Battery voltage [V]

- Pump current [mA]

- Potential temperature [K]

- Ozone mixing ratio per volume [ppm]

- Ozone number density [molecules/cm^3]

- Integrated ozone [DU] – there is some confusion about what is meant with this variable so define if carefully if you use it.

- Ice temperature [K]

- Dew point temperature [K]

- Water mixing ratio per volume [ppm]

- Pressure uncertainty estimate [hPa] (1 sigma)

- Geopotential height uncertainty estimate [gpm] (1 sigma)

- Ozone partial pressure uncertainty estimate [mPa] (1 sigma)

- Temperature uncertainty estimate [K] (1 sigma)

- Relative humidity uncertainty estimate [%] (1 sigma)

Real or integer auxiliary variables (in black: essential, in blue: nice, in red: optional):

- Number of levels

- NDACC ozonesonde data format version number

- This variable is designed to keep track of when the data formats have changed. If this variable were in the previous formats it would have a value of 1.0. For data files written with this new format, now recommended, we recommend starting with 2.0.

- Data version number of data owner

- This variable is designed to keep track of data versions and should be used if there is a significant change in the way the data are processed, e.g. if there was a difference in the way pump efficiency, or background current were incorporated. The definition is under full control of the corresponding owner!  We believe for most people who have not changed processing this number will be 1.0.

- Station longitude [decimal degrees E] (range: 0.00 – 359.99)

- Station latitude [decimal degrees N]

- Station height [m]

- Launch time (decimal UT hours from 0 hours on day given by DATE)

- Inverse pump flow rate [s/100 cm^3]

- Temperature during flow rate measurement [K]

- Relative humidity during flow rate measurement [%]

- Humidity correction to flow rate (negative: not applied; positive: applied).

- This number (> 1.0) represents the amount by which the flow rate is overestimated, or the time to pump 100 ml is underestimated.

- Inverse of pump efficiency at    2 hPa

- Inverse of pump efficiency at    3 hPa

- Inverse of pump efficiency at    5 hPa

- Inverse of pump efficiency at  10 hPa

- Inverse of pump efficiency at  20 hPa

- Inverse of pump efficiency at  30 hPa

- Inverse of pump efficiency at  50 hPa

- Inverse of pump efficiency at 100 hPa

- Inverse of pump efficiency at 200 hPa

- Inverse of pump efficiency at 300 hPa

- Inverse of pump efficiency at 500 hPa

- Inverse of pump efficiency at 1000 hPa

- Ozone background prior to exposure to ozone in laboratory Ib0 [microA]

- Ozone background after exposure to ozone in laboratory Ib1 [microA]

- Ozone background on filter just prior to launch Ib2 [microA]

- Ozone background used in calculation [microA]

- KI solution concentration [%]

- Buffer amount as a fraction of the buffer amount recommended by Komhyr 1986 for a solution with 10 g/l (1.0%) KI

- KBr amount as a fraction of the 25 g/l recommended in the Komhyr 1986 recipe for a solution of 1.0% KI

- Solution amount [cm^3]

- Column ozone from sonde [DU] (incl. residual ozone) (COL1)

- Residual ozone from sonde [DU]

- Remote sensed column ozone [DU] (COL2)

- Time of remote measurement (decimal UT hours from 0 hours on day given by DATE)

- Correction factor (COL2/COL1) (negative: not applied; positive: applied)

- Surface pressure correction (hPa)

- Surface temperature correction (K)

- Surface humidity correction (%)

- Surface pressure [hPa]

- Surface temperature [K]

- Surface dew point temperature [K]

- Surface wet-bulb temperature [K]

- Surface humidity [%]

- Surface wind direction [decimal degrees] (range: 0 – 360)

- Surface wind speed [m/s]

- Surface cloud cover [1/8]

- Surface ozone partial pressure measured prior to launch [mPa]

- Time run for surface ozone [min]

- Internal temperature prior to launch [K] (box or pump)

- Internal temperature during surface ozone measurement [K] (box or pump)

- Balloon weight [g]

- Balloon volume for plastic balloon [m^3, 0 for rubber balloon]

- Instrument and loadline weight (g)

- Free lift [g]

- Balance weight used for inflation [g]

- Maximum ozone partial pressure [mPa]

- Pressure level of maximum ozone partial pressure [hPa]

- Geopotential height of maximum ozone partial pressure [gpm]

- 1st tropopause height [gpm]

- Pressure at 1st tropopause height [hPa]

- Temperature at 1st tropopause height [K]

- 2nd tropopause height [gpm]

- Pressure at 2nd tropopause height [hPa]

- Temperature at 2nd tropopause height [K]

- Minimum pressure [hPa]

- Maximum geopotential height [gpm]

Character Auxiliary variables:

- Placeholder for transfer function applied

- Place of internal temperature sensor (box or pump)

- Background subtracted (Yes/No)

- Background subtraction constant or altitude dependent (constant/altitude dependent)

- If altitude dependent then there should be an explanation in the normal comment lines as to the formula used. For you information here is the formula used for altitude variation of background, attested to by many responses:

IBG = I0 * (A0 + A1*P + A2*P*P) / (A0 + A1*P0 + A2*P0*P0), where

P = ambient pressure, P0 = calibration pressure, I0 = sensor background current,

A0 = 1.23e-3, A1 = 1.24e-4, A2 = -2.69e-8.

- Ozonesonde type

- Serial number of ozonesonde

- Radiosonde type

- Flight number or data file name

- Serial number of radiosonde

- Serial number of interface card

- Lifting gas

- Balloon material

- Balloon brand

- Balloon type, e.g. TA/TX1200

- Balloon pretreatment

- Ground equipment

- Vertical averaging/smoothing method

- Heating method of box

- WMO station number

- Wavelength code of remote sensed column ozone

- Observation type of remote sensed column ozone

- Instrument of remote sensed column ozone

- Serial number of remote sensed column ozone

- Weather at launch

- Reason of discontinuation

- Column headings / heading units

- Column headings / heading units

- Column headings / heading units

- Column headings / heading units