Flight tasks (Stan)

Prepare recovery vehicle.

- Place the 4 antennas (3 freewave, 1 GPS) on the vehicle.

- Connect the 3 freewave radios. Includes antennas, power supplies (through power strip to inverter), and serial cables (Jupiter telemetry to back of computer, track packs to serial card).

- Plug the GPS into the computer

- And the computer power into the inverter

- Under the hood of UW270 – connect the second battery with the switch.

- Power up the invertor, computer, and radios to verify that the battery can power the system. If not connect a battery charger and/or secondary source (extension cord) to the system.

- Put the recovery equipment in the vehicle: Maps, Handheld GPS, Binoculars, ELPers, Ax, poles, chains, gloves…

- After checkout

  - power down systems,

  - turn off inverter,

  - disconnect computer (if temp<freezing) put computer in warm room.

Launch facility telemetery equipment

- Connect power to the computers and radios

- Check internet

- Move the extra antenna to the roof if necessary (for second MS/CN)

- Connect the antennas and preamp power to the radios (some of the labels here are old or do not exist – new labeling is needed)

- Verify that the wind speed & direction are reading on the weather system.

- Support Preflight checks –

  - Make sure the power cutoff switches are on

  - Verify instrument operation – during Jupiter and freewave checks verify that data is being received in the recovery vehicle.

  - Clear data system memory

  - Swap out batteries with new/charged batteries

  - Tape and seal the instrument boxes

- Tighten the straps

- Tie down the antenna poles

- Tape down loose wires

- Disconnect transponder power to insure there is no battery drain

Day of flight:

- Support Preflight checks –

- Verify that the telemetry equipment is working.

- Reconnect recovery computer if needed – power up recovery vehicle systems

- Reconnect transponder power

- Verify instrument operation – during Jupiter and freewave checks verify that data is being received in the recovery vehicle.

- Fill pi ball

- Check pressure on the helium tanks – determine which tanks we will use

- Prelaunch -

  - Connect  and layout the fill hoses

  - Connect power to the launcher (this may disconnect power to the recovery vehicle, so it may be a good time to start the vehicle and roll it outside)

  - On the fill hose – fill the balloon

  - Roll out the package

  - Layout the parachute and load line

  - Start the Argos system – verify gps lock

  - Check load line – Turn on strobe, turn on ELTs, dropper, start balloon track pack - verify

  - Start telemetry from instruments (including ozone) and verify that data is being received

  - Turn on package track pack – and verify

  - Verify transponder operation

- Launch -

  - Turn on pumps – verify data – ozone filters off – clear launch area

  - Top of the chute (the magic number is 5 – where ever the pi ball was at the count of 5, go to a point directly below that once the balloon is launched)

- After launch –

  - Verify that data is being received both upstairs and in the recovery vehicle

  - Get the latest estimated landing position

  - Load up the recovery vehicle and start the chase.